## Slide 1: CS 179: GPU Programming
Lecture 11 / Homework 4

## Slide 2: Breadth-First Search
Given source vertex S:
  Find min. #edges to reach every vertex from S
  (Assume source is vertex 0)
0
1
1
2
2
3
Sequential pseudocode:
  let Q be a queue
  Q.enqueue(source)
  label source as discovered
  source.value <- 0
  while Q is not empty
  v ← Q.dequeue()
  for all edges from v to w in G.adjacentEdges(v):
  if w is not labeled as discovered
  Q.enqueue(w)
  label w as discovered, w.value <- v.value + 1

## Slide 3: Alternate BFS algorithm
New sequential pseudocode:
  Input: Va, Ea, source (graph in “compact adjacency list” format)
  Create frontier (F), visited array (X), cost array (C)
  F <- (all false)
  X <- (all false)
  C <- (all infinity)
  F[source] <- true
  C[source] <- 0
  while F is not all false:
  for 0 ≤ i < |Va|:
  if F[i] is true:
  F[i] <- false
  X[i] <- true
  for Ea[Va[i]] ≤ j < Ea[Va[i+1]]:
  if X[j] is false:
  C[j] <- C[i] + 1
  F[j] <- true
Parallelizable!

## Slide 4: GPU-accelerated BFS
CPU-side pseudocode:
  Input: Va, Ea, source (graph in “compact adjacency list” format)
  Create frontier (F), visited array (X), cost array (C)
  F <- (all false)
  X <- (all false)
  C <- (all infinity)
  F[source] <- true
  C[source] <- 0
  while F is not all false:
  call GPU kernel( F, X, C, Va, Ea )
GPU-side kernel pseudocode:
  if F[threadId] is true:
  F[threadId] <- false
  X[threadId] <- true
  for Ea[Va[threadId]] ≤ j < Ea[Va[threadId + 1]]:
  if X[j] is false:
  C[j] <- C[threadId] + 1
  F[j] <- true
Can represent boolean values as integers

## Slide 5: Texture Memory (and co-stars)
Another type of memory system, featuring:
  Spatially-cached read-only access
  Avoid coalescing worries
  Interpolation
  (Other) fixed-function capabilities
  Graphics interoperability

## Slide 6: X-ray CT Reconstruction

## Slide 7: Medical Imaging
See inside people!
  Critically important in medicine today
"SaddlePE" by James Heilman, MD - Own work. Licensed under CC BY-SA 3.0 via Wikimedia Commons - http://commons.wikimedia.org/wiki/File:SaddlePE.PNG#/media/File:SaddlePE.PNG
"PAPVR". Licensed under CC BY 3.0 via Wikipedia - http://en.wikipedia.org/wiki/File:PAPVR.gif#/media/File:PAPVR.gif

## Slide 8: X-ray imaging (Radiography)
“Algorithm”:
  Generate electromagnetic radiation
  Measure radiation at the “camera”
Certain tissues are more “opaque” to X-rays
Like photography!
"Coude fp" by MB - Collection personnelle. Licensed under CC BY-SA 2.5 via Wikimedia Commons - http://commons.wikimedia.org/wiki/File:Coude_fp.PNG#/media/File:Coude_fp.PNG
http://www.imaginis.com/xray/how-does-x-ray-imaginig-work

## Slide 9: Radiography limitations
Generates 2D image of 3D body
What if we want a “slice” of 3D body?
  Goal: 3D reconstruction! (from multiple slices)
"Coude fp" by MB - Collection personnelle. Licensed under CC BY-SA 2.5 via Wikimedia Commons - http://commons.wikimedia.org/wiki/File:Coude_fp.PNG#/media/File:Coude_fp.PNG
"Computed tomography of human brain - large" by Department of Radiology, Uppsala University Hospital. Uploaded by Mikael Häggström. - Radiology, Uppsala University Hospital. Brain supplied by Mikael Häggström. It was taken Mars 23, 2007. Licensed under CC0 via Wikimedia Commons - http://commons.wikimedia.org/wiki/File:Computed_tomography_of_human_brain_-_large.png#/media/File:Computed_tomography_of_human_brain_-_large.png
vs.

## Slide 10: X-ray Computed Tomography (CT)
http://www.cancer.gov/
"Bonereconstruction" by Original uploader was Zgyorfi at en.wikipedia - Transferred from en.wikipedia; transferred to Commons by User:Common Good using CommonsHelper.. Licensed under CC BY-SA 3.0 via Wikimedia Commons - http://commons.wikimedia.org/wiki/File:Bonereconstruction.jpg#/media/File:Bonereconstruction.jpg

## Slide 11: X-ray Computed Tomography (CT)
Generate 2D “slice” using 3D imaging
  New imaging possibilities!
Reconstruction less straightforward

## Slide 12: X-ray Computed Tomography (CT)
http://www.thefullwiki.org/Basic_Physics_of_Nuclear_Medicine/X-Ray_CT_in_Nuclear_Medicine
“Algorithm” (per-slice):
  Take *lots* of pictures at different angles
    Each “picture” is a 1-D line
  Reconstruct the many 1-D pictures into a 2-D image
Harder, more computationally intensive!
  3D reconstruction requires multiple slices

## Slide 13: Mathematical Details
X-ray CT (per-slice) performs a 2D X-ray transform (eq. to 2D Radon transform):
  Suppose body density represented by within 2D slice,
  Assume linear attenuation of radiation
  For each line L of radiation measured by detector:
    : a unit vector in direction of L

## Slide 14: Mathematical Details
Defined as Lebesgue integral – non-oriented
  Opposite radiation direction should have same attenuation!
  Re-define as:

## Slide 15: Mathematical Details
  For each line L of radiation measured by detector:
Define general X-ray transform (for all lines L in R2):
  Fractional values of attenuation
  lies along L

## Slide 16: Mathematical Details
Define general X-ray transform:
  Parameterize
Redefine as:
  Define for

## Slide 17: Mathematical Details
Important properties:
  Many are redundant!
  Symmetry:
    Can define for

## Slide 18: X-ray Computed Tomography (CT)
Redefined X-ray transform, :
In reality:
  Only defined for some θ!

## Slide 19: X-ray CT Reconstruction
Given the results of our scan (the sinogram):
Obtain the original data: (“density” of our body)
In reality:
  This is hard
  We only scanned at certain (discrete) values of θ!
    Consequence: Perfect reconstruction is impossible!

## Slide 20: Reconstruction
…
X-ray emitter
X-ray detector

## Slide 21: Reconstruction
…
X-ray emitter
X-ray detector
Different θ’s

## Slide 22: Reconstruction
…
X-ray emitter
X-ray detector
Different θ’s
Each location on detector: Corresponds to multiple x0’s

## Slide 23: X-ray CT Reconstruction
Given the results of our scan (the sinogram):
Obtain the original data: (“density” of our body)
In reality:
  This is hard
  We only scanned at certain (discrete) values of θ!
    Consequence: Perfect reconstruction is impossible!

## Slide 24: Imperfect Reconstruction
10 angles of imaging
200 angles of imaging

## Slide 25: Reconstruction
Simpler algorithm – backprojection
  Not quite inverse Radon transform!
Claim: Can reconstruct image as:
  (θ’s where X-rays are taken)
  In other words: To reconstruct point, sum measurement along every line passing through that point

## Slide 26: Reconstruction
…
X-ray emitter
X-ray detector
Different θ’s
Each location on detector: Corresponds to multiple x0’s

## Slide 27: Geometry Details
For x0, need to find:
  At each θ, which radiation measurement corresponds to the line passing through x0?

## Slide 28: Geometry Details
Detector
Emitter
“The patient”
(slice)

## Slide 29: Geometry Details
(x0, y0)
Detector
Emitter
“The patient”
(slice)
θ

## Slide 30: Geometry Details
Detector
Emitter
“The patient”
(slice)
θ
Distance from sinogram centerline
d
(x0, y0)

## Slide 31: Geometry Details
Detector
Emitter
“The patient”
(slice)
θ
Radiation slope:
m = -cos(θ)/sin(θ)
Distance from sinogram centerline
d
(x0, y0)

## Slide 32: Geometry Details
Detector
Emitter
θ
Radiation slope:
m = -cos(θ)/sin(θ)
θ
Distance from sinogram centerline
d
Perpendicular slope:
q = -1/m (correction)
(x0, y0)

## Slide 33: Geometry Details
Detector
Emitter
θ
Radiation slope:
m = -cos(θ)/sin(θ)
θ
Distance from sinogram centerline
d
Perpendicular slope:
q = -1/m (correction)
(x0, y0)
Find intersection point (xi,yi)
Then d2 = xi2 + yi2
d

## Slide 34: Intersection point
Line 1: (point-slope)
Line 2:
Combine and solve:
Corrections

## Slide 35: Intersection point
Intersection point:
Distance from measurement centerline:
Corrections

## Slide 36: Geometry Details
Detector
Emitter
θ
Radiation slope:
m = -cos(θ)/sin(θ)
θ
Distance from sinogram centerline
d
Perpendicular slope:
q = -1/m (correction)
(x0, y0)
Find intersection point (xi,yi)
Then d2 = xi2 + yi2
d

## Slide 37: Sequential pseudocode
(input: X-ray sinogram):
(allocate output image)
for all y in image:
for all x in image:
for all theta in sinogram:
calculate m from theta
calculate x_i, y_i from m, -1/m
calculate d from x_i, y_i
image[x,y] += sinogram[theta, “distance”]
Clarification: Remember not to confuse geometric x,y with pixel x,y!
(0,0) geometrically is the center pixel of the image, and (0,0) in pixel coordinates is the upper left hand corner. Image is indexed row-wise
Correction/clarification:
d is the distance from the center of the sinogram – remember to center index appropriately
Use –d instead of d as appropriate (when -1/m > 0 and x_i < 0, or if -1/m < 0 and x_i > 0

## Slide 38: Sequential pseudocode
(input: X-ray sinogram):
(allocate output image)
for all y in image:
for all x in image:
for all theta in sinogram:
calculate m from theta
calculate x_i, y_i from m, -1/m
calculate d from x_i, y_i
image[x,y] += sinogram[theta, “distance”]
Parallelizable!
Inside loop depends only on x, y, theta
(corrections/clarification – see slide 37)

## Slide 39: Sequential pseudocode
(input: X-ray sinogram):
(allocate output image)
for all y in image:
for all x in image:
for all theta in sinogram:
calculate m from theta
calculate x_i, y_i from m, -1/m
calculate d from x_i, y_i
image[x,y] += sinogram[theta, “distance”]
For this assignment, only parallelize w/r/to x, y
(provides lots of parallelization already, other issues)
(corrections/clarification – see slide 37)

## Slide 40: Cautionary notes
y in an image is opposite of y geometrically!
  (Graphics/computing convention)
Edge cases (divide-by-0):
  θ = 0:
    d = x0
  θ = π/2:
    d = y0

## Slide 41: Almost a good reconstruction!
Original
Reconstruction

## Slide 42: Almost a good reconstruction!
“Backprojection blur”
  Similar to low-pass property of SMA (Week 1)
  We need an “anti-blur”! (opposite of Homework 1)

## Slide 43: Almost a good reconstruction!
Solution:
  A “high-pass filter”
  We can get frequency info in parallelizable manner!
    (FFT, Week 3)

## Slide 44: Almost a good reconstruction!
Solution:
  A “high-pass filter”
  We can get frequency info in parallelizable manner!
    (FFT, Week 3)

## Slide 45: High-pass filtering
Instead of filtering on image (2D HPF):
  Filter on sinogram! (1D HPF)
    (Equivalent reconstruction by linearity)
  Use cuFFT batch feature!
We’ll use a “ramp filter”
  Retained amplitude is
  linear function of frequency

## Slide 46: Almost a good reconstruction!
CPU-side:
(input: X-ray sinogram):
calculate FFT on sinogram using cuFFT
call filterKernel on freq-domain data
Calculate IFFT on freq-domain data
-> get new sinogram
GPU-side:
filterKernel:
Select specific freq-amplitude
based on thread ID
Get new amplitude from
ramp equation

## Slide 47: GPU Hardware
Non-coalesced access!
  Sinogram 0, index ~d0
  Sinogram 1, index ~d1
  Sinogram 2, index ~d2
  …
…

## Slide 48: GPU Hardware
Non-coalesced access!
  Sinogram 0, index ~d0
  Sinogram 1, index ~d1
  Sinogram 2, index ~d2
  …
However:
  Accesses are 2D spatially local!
…

## Slide 49: GPU Hardware
Solution:
  Cache sinogram in texture memory!
    Read-only (un-modified once we load it)
    Ignore coalescing
    2D spatial caching!
…

## Slide 50: Summary/pseudocode
(input: X-ray sinogram)
Filter sinogram (Slide 46)
Set up 2D texture cache on sinogram (Lecture 10):
Copy to CUDA array (2D)
Set addressing mode (clamp)
Set filter mode (linear, but won’t matter)
Set no normalization
Bind texture to sinogram
Calculate image backprojection (parallelize Slide 39)
Result: 200-250x speedup! (or more)

## Slide 51
Result: 200-250x speedup! (or more)

## Slide 52: Admin
This topic is harder than before!
  Lots of information
  I may have missed something
  If there’s anything unclear, let us know
    I can (and likely will) make additional slides/explanatory materials

## Slide 53: Admin
C/CUDA code should work on all machines
Pre/post-processing:
  Python scripts preprocess.py, postprocess.py
    (To run Python scripts: “python <script>.py”)
  Either:
    Use haru
    Install python, (optionally pip) -> numpy, scipy, matplotlib, scikit-image

## Slide 54: Resources
Imaging methods:
  X-Ray CT in Nuclear Medicine
  CT Image Reconstruction (Peters, at AAPM)
  Elements of Modern Signal Processing (Candes, at Stanford)
    Proof that our algorithm works!