## Slide 1
CS 179: GPU Programming
Lecture 1: Introduction
Images: http://en.wikipedia.org
http://www.pcper.com
http://northdallasradiationoncology.com/
GPU Gems (Nvidia)
Notes: 1

## Slide 2
Administration
Covered topics:
  (GP)GPU computing/parallelization
  C++ CUDA (parallel computing platform)
TAs:
  cs179.ta@gmail.com
  Parker Won (jwon@caltech.edu)
  Nailen Matchstick (nailen@caltech.edu)
  Jordan Bonilla (jbonilla@caltech.edu)
Website:
  http://courses.cms.caltech.edu/cs179/
Overseeing Instructor:
  Al Barr (barr@cs.caltech.edu)
Class time:
  ANB 105, MWF 3:00 PM
    Recitations on Fridays

## Slide 3
Course Requirements
Fill out this survey: https://goo.gl/forms/4GDYz4PtpcBr0qe03
Homework:
  6 weekly assignments
  Each worth 10% of grade
Final project:
  4-week project
  40% of grade total
P/F Students must receive at least 60% on every assignment AND the final project

## Slide 4
Homework
Due on Wednesdays before class (3PM)
Collaboration policy:
  Discuss ideas and strategies freely, but all code must be your own
Office Hours: Located in ANB 104
  Times: TBA (will be announced before first set is out)
Extensions
  Ask a TA for one if you have a valid reason

## Slide 5
Projects
Topic of your choice
  We will also provide many options
Teams of up to 2 people
  2-person teams will be held to higher expectations
Requirements
  Project Proposal
  Progress report(s) and Final Presentation
  More info later…

## Slide 6
Machines
Primary machine (multi-GPU):
  Currently being setup. You will gain access shortly after emailing cs179.ta@gmail.com
Secondary machines
  mx.cms.caltech.edu
  minuteman.cms.caltech.edu
  Use your CMS login
  NOTE: Not all assignments work on these machines
Change your password
  Use passwd command

## Slide 7
Machines
Alternative: Use your own machine:
  Must have an NVIDIA CUDA-capable GPU
  Virtual machines won’t work
    Exception: Machines with I/O MMU virtualization and certain GPUs
  Special requirements for:
    Hybrid/optimus systems
    Mac/OS X
Setup guide on the website is outdated. Do not follow 2016 instructions

## Slide 8
The CPU
The “Central Processing Unit”
Traditionally, applications use CPU for primary calculations
  General-purpose capabilities
  Established technology
  Usually equipped with 8 or less powerful cores
  Optimal for concurrent processes but not large scale parallel computations
Wikimedia commons: Intel_CPU_Pentium_4_640_Prescott_bottom.jpg

## Slide 9
The GPU
The "Graphics Processing Unit"
Relatively new technology designed for parallelizable problems
  Initially created specifically for graphics
  Became more capable of general computations

## Slide 10
GPUs – The Motivation
Raytracing:
for all pixels (i,j):
Calculate ray point and direction in 3d space
if ray intersects object:
calculate lighting at closest object
store color of (i,j)
Superquadric Cylinders, exponent 0.1, yellow glass balls, Barr, 1981

## Slide 11
EXAMPLE
Add two arrays
  A[ ] + B[ ] -> C[ ]
On the CPU:
  float *C = malloc(N * sizeof(float));
  for (int i = 0; i < N; i++)
  C[i] = A[i] + B[i];
  return C;
  This operates sequentially… can we do better?

## Slide 12
A simple problem…
On the CPU (multi-threaded, pseudocode):
  (allocate memory for C)
  Create # of threads equal to number of cores on processor (around 2, 4, perhaps 8)
  (Indicate portions of A, B, C to each thread...)
  ...
  In each thread,
  For (i from beginning region of thread)
  C[i] <- A[i] + B[i]
  //lots of waiting involved for memory reads, writes, ...
  Wait for threads to synchronize...
  This is slightly faster – 2-8x (slightly more with other tricks)

## Slide 13
A simple problem…
How many threads? How does performance scale?
Context switching:
  High penalty on the CPU
  Not an issue on the GPU

## Slide 14
A simple problem…
On the GPU:
  (allocate memory for A, B, C on GPU)
  Create the “kernel” – each thread will perform one (or a few) additions
  Specify the following kernel operation:
  For all i‘s (indices) assigned to this thread:
  C[i] <- A[i] + B[i]
  Start ~20000 (!) threads
  Wait for threads to synchronize...

## Slide 15
GPU: Strengths Revealed
Emphasis on parallelism means we have lots of cores
This allows us to run many threads simultaneously with no context switches

## Slide 16
GPU Computing: Step by Step
Setup inputs on the host (CPU-accessible memory)
Allocate memory for outputs on the host
Allocate memory for inputs on the GPU
Allocate memory for outputs on the GPU
Copy inputs from host to GPU
Start GPU kernel
Copy output from GPU to host
NOTE: Copying can be asynchronous

## Slide 17
The Kernel
Our “parallel” function
Given to each thread
Simple implementation:

## Slide 18
Indexing
Can get a block ID and thread ID within the block:
  Unique thread ID!

## Slide 19
Calling the Kernel

## Slide 20
Calling the Kernel (2)

## Slide 21
Questions?

## Slide 22
GPUs – Brief History
Initially based on graphics focused fixed-function pipelines
  Pre-set functions, limited options
http://gamedevelopment.tutsplus.com/articles/the-end-of-fixed-function-rendering-pipelines-and-how-to-move-on--cms-21469
Source: Super Mario 64, by Nintendo

## Slide 23
GPUs – Brief History
Shaders
  Could implement one’s own functions!
  GLSL (C-like language)
  Could “sneak in” general-purpose programming!
http://minecraftsix.com/glsl-shaders-mod/

## Slide 24
GPUs – Brief History
“General-purpose computing on GPUs” (GPGPU)
  Hardware has gotten good enough to a point where it’s basically having a mini-supercomputer
CUDA (Compute Unified Device Architecture)
  General-purpose parallel computing platform for NVIDIA GPUs
OpenCL (Open Computing Language)
  General heterogenous computing framework
Both are accessible as extensions to various languages
  If you’re into python, checkout theano