## Slide 1: CS 179: GPU Computing
Lecture 2: Intro to the simd lifestyle and GPU internals
Notes: Resume – remarks:
Welcome back
Storytelling/motivational purposes
Introducing

## Slide 2: Recap
Can use GPU to solve highly parallelizable problems
Straightforward extension to C++
  Separate CUDA code into .cu and .cuh files and compile with nvcc to create object files (.o files)
Looked at the a[] + b[] -> c[] example

## Slide 3: Recap
If you forgot everything, just make sure you understand that CUDA is simply an extension of other bits of code you write!!!!
  Evident in .cu/.cuh vs .cpp/.hpp distinction
  .cu/.cuh is compiled by nvcc to produce a .o file
  .cpp/.hpp is compiled by g++ and the .o file from the CUDA code is simply linked in using a "#include xxx.cuh" call
    No different from how you link in .o files from normal C++ code

## Slide 4
.cu/.cuh vs .cpp/.hpp

## Slide 5
.cu/.cuh vs .cpp/.hpp

## Slide 6
.cu/.cuh vs .cpp/.hpp

## Slide 7
.cu/.cuh vs .cpp/.hpp

## Slide 8: Thread Block Organization Keywords
  Keywords you MUST know to code in CUDA:
    Thread - Distributed by the CUDA runtime (threadIdx)
    Block - A user defined group of 1 to ~512 threads (blockIdx)
    Grid - A group of one or more blocks. A grid is created for each CUDA kernel function called
Notes: Point out how the different architectures have different thread per block counts.

## Slide 9: Block and Grid Dimensions
You can use a struct (defined in vector_types.h) called dim3 to define your Grid and Block dimensions.
dim3 grid(256); // defines a grid of 256 x 1 x 1 blocks
dim3 block(512, 512); // defines a block of 512 x 512 x 1 threads
foo<<<grid, block>>>(...);

## Slide 10: Grid/Block/Thread Visualized

## Slide 11: Single Instruction, Multiple Data (SIMD)
  SIMD describes a class of instructions which perform the same operation on multiple registers simultaneously.
  Example: Add some scalar to 3 registers, storing the output for each addition in those registers.
    Used to increase the brightness of a pixel
  CPUs also have SIMD instructions and are very important for applications that need to do a lot of number crunching
    Video codecs like x264/x265 make extensive use of SIMD instructions to speed up video encoding and decoding.

## Slide 12: SIMD continued
  Converting an algorithm to use SIMD is usually called “Vectorizing”
    Not every algorithm can benefit from this or even be vectorized at all, e.x. Parsing.
    Using SIMD instructions is not always beneficial though.
      Even using the SIMD hardware requires additional power, and thus waste heat.
      If the gains are small it probably isn’t worth the additional complexity.
    Optimizing compilers like GCC and LLVM are still being trained to be able to vectorize code usefully, though there has been many exciting developments on this front in the last 2 years and is an active area of study.
      https://polly.llvm.org/

## Slide 13: Thread blocks and Warps visualized
Copyright Games Workshop inc.

## Slide 14: Keywords you MUST know to code WELL in CUDA
    Streaming Multiprocessor – Each contains ~128 CUDA cores (which execute a thread) and their associated cache.
    Warp - A scheduling unit of up to 32 threads (all within the same block)
    Warp Divergence – A condition where threads within a warp need to execute different instructions in order to continue executing their kernel.
      Causes threads to execute sequentially, in most cases ruining parallel performance
      As of the Kepler (2012) architecture each Warp can have at most 2 branches, starting with Volta (2017) this condition has been nearly eliminated. For this class assume your code must only branch at most twice as we are not yet allocating Volta GPUs to this class.

## Slide 15: What a modern GPU looks like

## Slide 16: Inside a GPU
The black Xs are just crossing out things you don’t have to think about just yet. You'll learn about them later

## Slide 17: Inside a GPU
Think of Device Memory (we will also refer to it as Global Memory) as a RAM for your GPU
  Faster than getting memory from the actual RAM but still can be faster
  Will come back to this in future lectures
GPUs have many Streaming Multiprocessors (SMs)
  Each SM has multiple processors but only one instruction unit
  Groups of processors must run the exact same set of instructions at any given time with in a single SM

## Slide 18: Inside a GPU
When a kernel (the thing you define in .cu files) is called, the task is divided up into threads
  Each thread handles a small portion of the given task
The threads are divided into a Grid of Blocks
  Both Grids and Blocks are 3 dimensional
  e.g.
  dim3 dimBlock(8, 8, 8);
  dim3 dimGrid(100, 100, 1);
  Kernel<<<dimGrid, dimBlock>>>(…);
  However, we'll often only work with 1 dimensional grids and blocks
  e.g. Kernel<<<block_count, block_size>>>(…);

## Slide 19: Inside a GPU
Maximum number of threads per block count is usually 512 or 1024 depending on the machine
Maximum number of blocks per grid is usually 65535
  If you go over either of these numbers your GPU will just give up or output garbage data
  Much of GPU programming is dealing with this kind of hardware limitations! Get used to it
  This limitation also means that your Kernel must compensate for the fact that you may not have enough threads to individually allocate to your data points
    Will show how to do this later (this lecture)

## Slide 20: Inside a GPU
Each block is assigned to an SM
Inside the SM, the block is divided into Warps of threads
  Warps consist of 32 threads
  All 32 threads MUST run the exact same set of instructions at the same time
    Due to the fact that there is only one instruction unit
  Warps are run concurrently in an SM
  If your Kernel tries to have threads do different things in a single warp (using if statements for example), the two tasks will be run sequentially
    Called Warp Divergence (NOT GOOD)

## Slide 21: Inside a GPU (fun hardware info)
In Fermi Architecture (i.e. GPUs with Compute Capability 2.x), each SM has 32 cores, later architectures have more.
  e.g. GTX 400, 500 series
  32 cores is not what makes each warp have 32 threads. Previous architecture also had 32 threads per warp but had less than 32 cores per SM
  Some early Pascal (2016) GPUs (GP100) had 64 cores per SM, but later chips in that generation (GP104) had 128 core model.

## Slide 22: Streaming Multiprocessor
Shown here is a Pascal GP104 GPU Streaming Multiprocessor that can be found in a GTX1080 graphics card.
The exact amount of Cache and Shared Memory differ between GPU models, and even more so between different architectures.
  Whitepapers with exact information can be gotten from Nvidia (use Google)
  https://international.download.nvidia.com/geforce-com/international/pdfs/GeForce_GTX_1080_Whitepaper_FINAL.pdf
  http://www.nvidia.com/content/PDF/product-specifications/GeForce_GTX_680_Whitepaper_FINAL.pdf
  “nvidia kepler whitepaper”

## Slide 23
A[] + B[] -> C[] (again)

## Slide 24
A[] + B[] -> C[] (again)

## Slide 25
A[] + B[] -> C[] (again)

## Slide 26: Questions so far?

## Slide 27
Stuff that will be useful later

## Slide 28
Stuff that will be useful later

## Slide 29
Stuff that will be useful later

## Slide 30: Next Time...
Global Memory access is not that fast
  Tends to be the bottleneck in many GPU programs
  Especially true if done stupidly
    We'll look at what "stupidly" means
Optimize memory access by utilizing hardware specific memory access patterns
Optimize memory access by utilizing different caches that come with the GPU