## Slide 1: Congestion Control & Optimization
Steven Low
netlab.CALTECH.edu
Cambridge 2011

## Slide 2: Acknowledgments
Caltech: L. Chen, J. Doyle, C. Jin, G. Lee, H. Newman, A. Tang, D. Wei, B. Wydrowski, Netlab Gen1
Uruguay: F. Paganini
Swinburne: L. Andrew
Princeton: M. Chiang

## Slide 3: Goal of tutorial
Top-down summary of congestion control on Internet
Introduction to mathematical models of congestion control
Illustration of theory-guided CC algorithm design

## Slide 4: Theory-guided design
Tight integration of theory, design, experiment
  Analysis done at design time, not after
Theory does not replace intuitions or heuristics
  Refines, validates/invalidates them
Theory provides structure and clarity
  Guides design
  Suggests ideas and experiments
  Explores boundaries that are hard to experiment

## Slide 5: Theory-guided design
Integration of theory, design, experiment can be very powerful
  Each needs the other
  Combination much more than sum
Tremendous progress in the last decade
  Not as impossible as most feared
  Very difficult; but worth the effort
  Most critical: mindset
How to push theory-guided design approach further ?
Notes: After FR/FR, when CA is entered, cwnd is half of the window when lost was detected.
So the effect of lost is halving the window.
[Source: RFC 2581, Fall & Floyd, “Simulation based Comparison of Tahoe, Reno, and SACK TCP”]

## Slide 6: Agenda
9:00 Congestion control protocols
10:00 break
10:15 Mathematical models
11:15 break
11:30 Advanced topics
12:30 lunch

## Slide 7: Audience background
Know TCP/IP protocols?
Know congestion control?
Experiment with ns2? Linux kernel?
Know optimization theory? Control theory?
Know network utility maximization?

## Slide 8: Congestion Control Protocols

## Slide 9: Congestion control protocols
Why congestion control?
Where is CC implemented?
Window control mechanism
CC protocols and basic structure
Active queue management (AQM)

## Slide 10: Congestion collapse
October 1986, the first congestion collapse on the Internet was detected
Link between UC Berkeley and LBL
  400 yards, 3 hops, 32 Kbps
  throughput dropped to 40 bps
  factor of ~1000 drop!
1988, Van Jacobson proposed TCP congestion control
WHY ?
throughput
load

## Slide 11: Network milestones
1969
1974
ARPANet
1988
TCP
2006
81
TCP/IP
50-56kbps, ARPANet
Backbone speed:
T1
NSFNet
1991
T3, NSFNet
1996
1999
OC12
MCI
OC48
vBNS
2003
OC192
Abilene
HTTP
Tahoe
Network is exploding
83
Cutover
to TCP/IP
Notes: HEP = High Energy Physics – most recent demonstration was a few weeks ago where the team achieved a peak through put of 151 Gpbs and sustained through put of over 100 Gpbs

## Slide 12: Application milestones
1969
ARPANet
1988
TCP
81
TCP/IP
50-56kbps, ARPANet
T1
NSFNet
OC12
MCI
T3, NSFNet
OC48
vBNS
OC192
Abilene
HTTP
Tahoe
83
Cutover
to TCP/IP
1969
1972
1988
Tahoe
1971
ARPANet
Network
Mail
1973
File
Transfer
Telnet
Simple applications
1993
2005
1995
Internet
Phone
Whitehouse
online
Internet
Talk
Radio
Diverse & demanding applications
1990
Napster
music
2004
AT&T
VoIP
iTunes
video
YouTube
Notes: HEP = High Energy Physics – most recent demonstration was a few weeks ago where the team achieved a peak through put of 151 Gpbs and sustained through put of over 100 Gpbs

## Slide 13: Network Mail (1971)
First Internet (ARPANet) application
The first network email was sent by Ray Tomlinson between these two
computers at BBN that are connected by the ARPANet.

## Slide 14: Internet applications (2006)
Telephony
Music
TV & home theatre
Cloud computing
Finding your way
Mail
Friends
Library at your finger tip
Games

## Slide 15: Congestion collapse
1969
ARPANet
1988
TCP
81
TCP/IP
50-56kbps, ARPANet
T1
NSFNet
OC12
MCI
T3, NSFNet
OC48
vBNS
OC192
Abilene
HTTP
Tahoe
83
Cutover
to TCP/IP
1969
1988
Tahoe
ARPANet
Network
Mail
File
Transfer
Telnet
1993
1995
Internet
Phone
Whitehouse
online
Internet
Talk
Radio
1990
Napster
music
2004
AT&T
VoIP
iTunes
video
YouTube
1974
1969
1988
2006
1983
TCP/IP
ARPANet
TCP
congestion collapse
detected at LBL
Notes: HEP = High Energy Physics – most recent demonstration was a few weeks ago where the team achieved a peak through put of 151 Gpbs and sustained through put of over 100 Gpbs

## Slide 16: Congestion collapse
October 1986, the first congestion collapse on the Internet was detected
Link between UC Berkeley and LBL
  400 yards, 3 hops, 32 Kbps
  throughput dropped to 40 bps
  factor of ~1000 drop!
1988, Van Jacobson proposed TCP congestion control
throughput
load

## Slide 17: Why the 1986 collapse
congestion collapse
detected at LBL

## Slide 18: Why the 1986 collapse
5,089 hosts on Internet (Nov 1986)
Backbone speed: 50 – 56 kbps
Control mechanism focused only on receiver congestion, not network congestion
Large number of hosts sharing a slow (and small) network
  Network became the bottleneck, as opposed to receivers
  But TCP flow control only prevented overwhelming receivers
Jacobson introduced feedback control to
deal with network congestion in 1988

## Slide 19: Tahoe and its variants (1988)
Jacobson, Sigcomm 1988
+ Avoid overwhelming network
+ Window control mechanisms
  Dynamically adjust sender window based on congestion (as well as receiver window)
  Loss-based AIMD
  Based on idea of Chiu, Jain, Ramakrishnan
“… important considering that TCP spans a range from 800 Mbps Cray channels to 1200 bps packet radio links”
-- Jacobson, 1988

## Slide 20: TCP congestion control
1969
ARPANet
1988
TCP
81
TCP/IP
50-56kbps, ARPANet
T1
NSFNet
OC12
MCI
T3, NSFNet
OC48
vBNS
OC192
Abilene
HTTP
Tahoe
83
Cutover
to TCP/IP
1969
1988
Tahoe
ARPANet
Network
Mail
File
Transfer
Telnet
1993
1995
Internet
Phone
Whitehouse
online
Internet
Talk
Radio
1990
Napster
music
2004
AT&T
VoIP
iTunes
video
YouTube
1974
1969
1988
2006
1983
TCP/IP
ARPANet
Flow control:
Prevent overwhelming receiver
+ Congestion control:
Prevent overwhelming network
Tahoe
TCP
congestion collapse
detected at LBL
Notes: HEP = High Energy Physics – most recent demonstration was a few weeks ago where the team achieved a peak through put of 151 Gpbs and sustained through put of over 100 Gpbs

## Slide 21: Transport milestones
1974
1969
1988
2006
1983
TCP/IP
ARPANet
TCP
DECNet
AIMD
‘94
Vegas
delay
based
Tahoe
‘96
formula
‘98
NUM
‘00
reverse
engr TCP
systematic
design
of TCPs
Notes: HEP = High Energy Physics – most recent demonstration was a few weeks ago where the team achieved a peak through put of 151 Gpbs and sustained through put of over 100 Gpbs

## Slide 22: Congestion control protocols
Why congestion control?
Where is CC implemented?
Window control mechanism
CC protocols and basic structure
Active queue management (AQM)

## Slide 23: Packet networks
Packet-switched as opposed to circuit-switched
  No dedicated resources
  Simple & robust: states in packets
More efficient sharing of resources
  Multiplexing gain
Less guarantee on performance
  Best effort

## Slide 24: Network mechanisms
Transmit bits across a link
  encoding/decoding, mod/dem, synchronization
Medium access
  who transmits when for how long
Routing
  choose path from source to destination
Loss recovery
  recover packet loss due to congestion, error, interference
Flow/congestion control
  efficient use of bandwidth/buffer without overwhelming receiver/network

## Slide 25: Protocol stack
Network mechanisms implemented as protocol stack
Each layer designed separately, evolves asynchronously
application
transport
network
link
physical
Many control mechanisms…
Error control, congestion control (TCP)
Routing (IP)
Medium access control
Coding, transmission, synchronization
Notes: Network adopts a layered architecture. As a result, protocol stack for network has five layers: application, transport, network, link and physical layers. Each layer is designed separately and usually abstracted as an optimization problem. For example, TCP can be seen as a distributed algorithm to solve utility maximization problem, intradomain routing is to solve minimum cost problem. The main reason to choose a layered structure is to manage the design complexity. This has been justified by the success of communication network.

## Slide 26: The Internet hourglass
IP
Web
Search
Mail
News
Video
Audio
Friends
Applications
TCP
Ethernet
802.11
Satellite
Optical
3G/4G
Bluetooth
ATM
Link technologies

## Slide 27: IP layer
Routing from source to destination
  Distributed computation of routing decisions
  Implemented as routing table at each router
  Shortest-path (Dijkstra) algorithm within an autonomous system
  BGP across autonomous systems
Datagram service
  Best effort
  Unreliable: lost, error, out-of-order
Simple and robust
  Robust against failures
  Robust against, and enables, rapid technological evolution above & below IP

## Slide 28: TCP layer
End-to-end reliable byte stream
  On top of unreliable datagram service
  Correct, in-order, without loss or duplication
Connection setup and tear down
  3-way handshake
Loss and error recovery
  CRC to detect bit error
  Sequence number to detect packet loss/duplication
  Retransmit packets lost or contain errors
Congestion control
  Source-based distributed control

## Slide 29: Protocol data format
Applications (e.g. Telnet, HTTP)
TCP
UDP
ICMP
ARP
IP
Link Layer (e.g. Ethernet, ATM)
Physical Layer (e.g. Ethernet, SONET)

## Slide 30: Protocol data format
Application Message
TCP data
TCP hdr
MSS
TCP Segment
IP data
IP hdr
IP Packet
Ethernet data
Ethernet
Ethernet Frame
20 bytes
20 bytes
14 bytes
4 bytes
MTU 1500 bytes

## Slide 31: IP Header
0 1 2 3
Vers(4)
Flags
H len
Type of Service
Total Length (16 bits)
Fragment Offset
Identification
Header Checksum
Protocol (TCP=6)
Time to Live
Source IP Address
Destination IP Address
Options
Padding
IP data

## Slide 32: TCP Header
Source Port
Destination Port
Sequence Number (32 bits)
Checksum
Options
Padding
Acknowledgement Number (32 bits)
Urgent Pointer
URG
ACK
PSH
RST
SYN
FIN
Data
Offset
Reserved
Receive Window (16 bits)
TCP data
0 1 2 3

## Slide 33: Congestion control protocols
Why congestion control?
Where is CC implemented?
Window control mechanism
CC protocols and basic structure
Active queue management (AQM)

## Slide 34: Window control
~ W packets per RTT
Lost packet detected by missing ACK
Self-clocking: regulates flow
RTT
time
time
Source
Destination
1
2
W
1
2
W
1
2
W
data
ACKs
1
2
W

## Slide 35: Source rate
Limit the number of packets in the network to window W
Source rate = bps
If W too small then rate < capacity
else rate > capacity ( congestion)
How to decide W?

## Slide 36: Early TCP
Pre 1988
Go-back-N ARQ
  Detects loss from timeout
  Retransmits from lost packet onward
Receiver window flow control
  Prevents overflow at receive buffer
  Receiver sets awnd in TCP header of each ACK
    Closes when data received and ack’ed
    Opens when data delivered to application
  Sender sets W = awnd
Self-clocking

## Slide 37: TCP congestion control
Post 1988
ARQ, awnd from ACK, self-clocking
In addition:
Source calculates cwnd from indication of network congestion
  Packet loss
  Packet delay
  Marks, explicit congestion notification
Source sets W = min (cwnd, awnd)
Algorithms to calculate cwnd
  Reno, Vegas, FAST, CUBIC, CTCP, …

## Slide 38: Congestion control protocols
Why congestion control?
Where is CC implemented?
Window control mechanism
CC protocols and basic structure
Active queue management (AQM)

## Slide 39: Key references
TCP/IP spec
RFC 791 Internet Protocol
RFC 793 Transmission Control Protocol
AIMD idea: Chiu, Jain, Ramakrishnan 1988-90
Tahoe/Reno: Jacobson 1988
Vegas: Brakmo and Peterson 1995
FAST: Jin, Wei, Low 2004
CUBIC: Ha, Rhee, Xu 2008
CTCP: Kun et al 2006
RED: Floyd and Jacobson 1993
REM: Athuraliya, Low, Li, Yin 2001
There are many many other proposals and references

## Slide 40: TCP Congestion Control
Has four main parts
  Slow Start (SS)
  Congestion Avoidance (CA)
  Fast Retransmit
  Fast Recovery
ssthresh: slow start threshold determines whether to use SS or CA
Assumption: packet losses are caused by buffer overflow (congestion)
Tahoe
Reno

## Slide 41: TCP Tahoe (Jacobson 1988)
SS
time
window
CA
SS: Slow Start
CA: Congestion Avoidance

## Slide 42: TCP Reno (Jacobson 1990)
CA
SS
Fast retransmission/fast recovery

## Slide 43: Slow Start
Start with cwnd = 1 (slow start)
On each successful ACK increment cwnd
cwnd  cnwd + 1
Exponential growth of cwnd
each RTT: cwnd  2 x cwnd
Enter CA when cwnd >= ssthresh

## Slide 44: Slow Start
data packet
ACK
receiver
sender
1 RTT
cwnd
1
2
3
4
5
6
7
8
cwnd  cwnd + 1 (for each ACK)

## Slide 45: Congestion Avoidance
Starts when cwnd  ssthresh
On each successful ACK:
cwnd  cwnd + 1/cwnd
Linear growth of cwnd
each RTT: cwnd  cwnd + 1

## Slide 46: Congestion Avoidance
cwnd
1
2
3
1 RTT
4
data packet
ACK
receiver
sender
cwnd  cwnd + 1 (for cwnd worth of ACKs)

## Slide 47: Packet Loss
Assumption: loss indicates congestion
Packet loss detected by
  Retransmission TimeOuts (RTO timer)
  Duplicate ACKs (at least 3)
1
2
3
4
5
6
1
2
3
Packets
Acknowledgements
3
3
7
3

## Slide 48: Fast Retransmit/Fast Recovery
Motivation
  Waiting for timeout is too long
  Prevent `pipe’ from emptying during recovery
Idea
  3 dupACKs indicate packet loss
  Each dupACK also indicates a packet having left the pipe (successfully received)!
Notes: After FR/FR, when CA is entered, cwnd is half of the window when lost was detected.
So the effect of lost is halving the window.
[Source: RFC 2581, Fall & Floyd, “Simulation based Comparison of Tahoe, Reno, and SACK TCP”]

## Slide 49: Fast Retransmit/Fast Recovery
Enter FR/FR after 3 dupACKs
  Set ssthresh  max(flightsize/2, 2)
  Retransmit lost packet
  Set cwnd  ssthresh + ndup (window inflation)
  Wait till W=min(awnd, cwnd) is large enough; transmit new packet(s)
  On non-dup ACK (1 RTT later), set cwnd  ssthresh (window deflation)
Enter CA (unless timeout)
Notes: After FR/FR, when CA is entered, cwnd is half of the window when lost was detected.
So the effect of lost is halving the window.
[Source: RFC 2581, Fall & Floyd, “Simulation based Comparison of Tahoe, Reno, and SACK TCP”]

## Slide 50: Example: FR/FR
Fast retransmit
  Retransmit on 3 dupACKs
Fast recovery
  Inflate window while repairing loss to fill pipe
1
2
time
S
time
D
3
4
5
6
8
7
1
1
1
1
1
1
9
9
1
1
0
1
11
Exit FR/FR
RTT
8
7
window inflation
4
window deflates

## Slide 51: Summary: Reno
Basic idea
  AIMD probes available bandwidth
  Fast recovery avoids slow start
  dupACKs: fast retransmit + fast recovery
  Timeout: fast retransmit + slow start
slow start
retransmit
congestion avoidance
FR/FR
dupACKs
timeout

## Slide 52: Delay-based TCP: Vegas (Brakmo & Peterson 1994)
Reno with a new congestion avoidance algorithm
Converges (provided buffer is large) !
SS
time
window
CA

## Slide 53: TCP CC variants
Differ mainly in Congestion Avoidance
  Vegas: delay-based
  FAST: delay-based, scalable
  CUBIC: time since last congestion
  CTCP: use both loss & delay
slow start
retransmit
congestion avoidance
FR/FR
dupACKs
timeout

## Slide 54: Congestion avoidance
for every ACK {
W += 1/W (AI)
}
for every loss {
W = W/2 (MD)
}
Reno
Jacobson
1988
for every ACK {
if W/RTTmin – W/RTT < a then W ++
if W/RTTmin – W/RTT > b then W --
}
for every loss {
W = W/2
}
Vegas
Brakmo
Peterson
1995

## Slide 55: Congestion avoidance
FAST
Jin, Wei, Low
2004
periodically
{
}

## Slide 56: Congestion control protocols
Why congestion control?
Where is CC implemented?
Window control mechanism
CC protocols and basic structure
Active queue management (AQM)

## Slide 57: Feedback control
xi(t)
pl(t)
Example congestion measure pl(t)
  Loss (Reno)
  Queueing delay (Vegas)

## Slide 58: TCP/AQM
Congestion control is a distributed asynchronous algorithm to share bandwidth
It has two components
  TCP: adapts sending rate (window) to congestion
  AQM: adjusts & feeds back congestion information
They form a distributed feedback control system
  Equilibrium & stability depends on both TCP and AQM
  And on delay, capacity, routing, #connections
pl(t)
xi(t)
TCP:
Reno
Vegas
FAST
AQM:
DropTail
RED
REM/PI
AVQ

## Slide 59: Implicit feedback
Drop-tail
  FIFO queue
  Drop packet that arrives at a full buffer
Implicit feedback
  Queueing process implicitly computes and feeds back congestion measure
  Delay: simple dynamics
  Loss: no convenient model

## Slide 60: Active queue management
Explicit feedback
  Provide congestion information by probabilistically marking packets
  2 ECN bit in IP header allocated for AQM
Supported by all new routers but usually turned off in the field

## Slide 61: RED (Floyd & Jacobson 1993)
Congestion measure: average queue length
bl(t+1) = [bl(t) + yl(t) - cl]+
rl(t+1) = (1-a) rl(t) + a bl(t)
Embedding: p-linear probability function
Feedback: dropping or ECN marking
Avg queue
marking
1

## Slide 62: REM (Athuraliya & Low 2000)
Congestion measure: price
bl(t+1) = [bl(t) + yl(t) - cl]+
pl(t+1) = [pl(t) + g(al bl(t)+ xl (t) - cl )]+
Embedding: exponential probability function
Feedback: dropping or ECN marking

## Slide 63: REM
Match rate
Clear buffer and match rate
Clear buffer
Sum prices
Theorem (Paganini 2000)
Global asymptotic stability for general utility function (in the absence of delay)

## Slide 64: Summary: CC protocols
End-to-end CC implemented in TCP
  Basic window mechanism
  TCP performs connection setup, error recovery, and congestion control,
  CC dynamically computes cwnd that limits max #pkts enroute
Distributed feedback control algorithm
  TCP: adapts congestion window
  AQM: adapts congestion measure
Notes: After FR/FR, when CA is entered, cwnd is half of the window when lost was detected.
So the effect of lost is halving the window.
[Source: RFC 2581, Fall & Floyd, “Simulation based Comparison of Tahoe, Reno, and SACK TCP”]

## Slide 65: Agenda
9:00 Congestion control protocols
10:00 break
10:15 Mathematical models
11:15 break
11:30 Advanced topics
12:30 lunch

## Slide 66: Mathematical Models

## Slide 67: Mathematical models
Why mathematical models?
Dynamical systems model of CC
Convex optimization primer
Reverse engr: equilibrium properties
Forward engr: FAST TCP

## Slide 68: Why mathematical models
Protocols are critical, yet difficult, to understand and optimize
Local algorithms, distributed spatially and vertically  global behavior
Designed separately, deployed asynchronously, evolves independently
application
transport
network
link
physical

## Slide 69: Why mathematical models
Need systematic way to understand, design, and optimize
Their interactions
Resultant global behavior
application
transport
network
link
physical

## Slide 70: Why mathematical models
Not to replace intuitions, expts, heuristics
Provides structure and clarity
  Refines intuition
  Guides design
  Suggests ideas
  Explores boundaries
  Understands structural properties
Risk
  “All models are wrong”
  “… some are useful”
  Validate with simulations & experiments

## Slide 71: Structural properties
Equilibrium properties
  Throughput, delay, loss, fairness
Dynamic properties
  Stability
  Robustness
  Responsiveness
Scalability properties
  Information scaling (decentralization)
  Computation scaling
  Performance scaling

## Slide 72
L., Peterson, Wang, JACM 2002
Notes: Before ~2000, no one in the world can predict the throughputs of a set of TCP flows sharing a simple network (that’s more than a single bottleneck), despite a decade of research. With the theory developed in the last decade or so, we can now predict the throughput, delay, loss in an arbitrary TCP network (under appropriate assumptions). Here is one example.

## Slide 73: Limitations of basic model
Static and deterministic network
  Fixed set of flows, link capacities, routing
  Real networks are time-varying and random
Homogeneous protocols
  All flows use the same congestion measure
Fluid approximation
  Ignore packet level effects, e.g. burstiness
  Inaccurate buffering process
Difficulty in analysis of model
  Global stability in presence of feedback delay
  Robustness, responsiveness
basic model has been generalized
to address these issues to various degrees

## Slide 74: Mathematical models
Why mathematical models?
Dynamical systems model of CC
Convex optimization primer
Reverse engr: equilibrium properties
Forward engr: FAST TCP

## Slide 75: TCP/AQM
Congestion control is a distributed asynchronous algorithm to share bandwidth
It has two components
  TCP: adapts sending rate (window) to congestion
  AQM: adjusts & feeds back congestion information
They form a distributed feedback control system
  Equilibrium & stability depends on both TCP and AQM
  And on delay, capacity, routing, #connections
pl(t)
xi(t)
TCP:
Reno
Vegas
FAST
AQM:
DropTail
RED
REM/PI
AVQ

## Slide 76: Network model
p1(t)
p2(t)
Network
  Links l of capacities cl and congestion measure pl(t)
Sources i
  Source rates xi(t)
Routing matrix R
x1(t)
x2(t)
x3(t)

## Slide 77: Network model
F1
FN
G1
GL
R
RT
TCP
Network
AQM
x
y
q
p
Reno, Vegas
Droptail, RED
IP routing
TCP CC model consists of
specs for Fi and Gl

## Slide 78: Examples
Derive (Fi, Gl) model for
  Reno/RED
  Vegas/Droptail
  FAST/Droptail
Focus on Congestion Avoidance

## Slide 79: Model: Reno
for every ack (ca)
{ W += 1/W }
for every loss
{ W := W/2 }

## Slide 80: Model: Reno
for every ack (ca)
{ W += 1/W }
for every loss
{ W := W/2 }
link loss
probability
round-trip
loss probability
window size
throughput

## Slide 81: Model: Reno
for every ack (ca)
{ W += 1/W }
for every loss
{ W := W/2 }

## Slide 82: Model: RED
queue length
marking prob
1
source
rate
aggregate
link rate

## Slide 83: Model: Reno/RED

## Slide 84: Decentralization structure
F1
FN
G1
GL
R
RT
TCP
Network
AQM
x
y
q
p
q
y

## Slide 85: Validation – Reno/REM
30 sources, 3 groups with RTT = 3, 5, 7 ms
Link capacity = 64 Mbps, buffer = 50 kB
Smaller window due to small RTT (~0 queueing delay)
Notes: Same scenario as Reno
3 groups of 10 sources each, with RTT (propagation delay + queueing, from measurement) 9, 11 & 13 ms.
Group 1 starts at time 0, group 2 starts at time 500, and group 3 starts at time 1000.
Graph shows the mean window process, averaged over the 10 sources of each group.
Window is in unit of packets, each of size 1kBytes.
Note
  Windows are equalized, independent of RTTs
  Measured windows match well with those predicted by the model
Note: Individual windows were halved on each decrement, but the graph shows the window process averaged over 10 sources in each group.

## Slide 86: Queue
DropTail
queue = 94%
RED
min_th = 10 pkts
max_th = 40 pkts
max_p = 0.1
p = Lagrange multiplier!
p increasing in queue!
REM
queue = 1.5 pkts
utilization = 92%
g = 0.05, a = 0.4, f = 1.15
p decoupled from queue
Notes: 30 sources, 3 groups with RTT = 3, 5, 7ms + 6ms (queueing delay) Link capacity = 64 Mbps, buffer = 50 kB
3 groups of 10 sources each, with RTT (propagation delay + queueing, from measurement) 9, 11 & 13 ms.
Group 1 starts at time 0, group 2 starts at time 500, and group 3 starts at time 1000.
Graph shows the mean window process, averaged over the 10 sources of each group.
Window is in unit of packets, each of size 1kBytes.
Note
  Windows are equalized, independent of RTTs
  Measured windows match well with those predicted by the model
Note: Individual windows were halved on each decrement, but the graph shows the window process averaged over 10 sources in each group.

## Slide 87: Model: Vegas/Droptail
queue size
for every RTT
{ if W/RTTmin – W/RTT < a then W ++
if W/RTTmin – W/RTT > a then W -- }
for every loss
W := W/2
Fi:
pl(t+1) = [pl(t) + yl (t)/cl - 1]+
Gl:

## Slide 88: Model: FAST/Droptail
periodically
{
}

## Slide 89
L., Peterson, Wang, JACM 2002
Notes: Before ~2000, no one in the world can predict the throughputs of a set of TCP flows sharing a simple network (that’s more than a single bottleneck), despite a decade of research. With the theory developed in the last decade or so, we can now predict the throughput, delay, loss in an arbitrary TCP network (under appropriate assumptions). Here is one example.

## Slide 90: Validation: matching transients
Same RTT, no cross traffic
Same RTT, cross traffic
Different RTTs, no cross traffic
[Jacobsson et al 2009]

## Slide 91: Recap
Protocol (Reno, Vegas, FAST, Droptail, RED…)
Equilibrium
Performance
  Throughput, loss, delay
Fairness
Utility
Dynamics
Local stability
Global stability

## Slide 92: Mathematical models
Why mathematical models?
Dynamical systems model of CC
Convex optimization primer
Reverse engr: equilibrium properties
Forward engr: FAST TCP

## Slide 93: Background: optimization
Called convex program if Ui are concave functions

## Slide 94: Background: optimization
Called convex program if Ui are concave functions
Local optimum is globally optimal
  First order optimality (KKT) condition is necessary and sufficient
Convex programs are polynomial-time solvable
  Whereas nonconvex programs are generally NP hard

## Slide 95: Background: optimization
Theorem
Optimal solution x* exists
It is unique if Ui are strictly concave
strictly concave
not

## Slide 96: Background: optimization
Theorem
x* is optimal if and only if there exists such that
Lagrange
multiplier
Complementary
slackness: all
bottlenecks are
fully utilized

## Slide 97: Background: optimization
Theorem
p* can be interpreted as prices
  Optimal maximizes its own benefit
incentive compatible

## Slide 98: Background: optimization
Theorem
Gradient decent algorithm to solve the dual problem is decentralized
law of supply & demand

## Slide 99: Background: optimization
Theorem
Gradient decent algorithm to solve the dual problem is decentralized
Gradient-like algorithm to solve NUM
defines TCP CC algorithm !
reverse/forward
engineer TCP

## Slide 100: Mathematical models
Why mathematical models?
Dynamical systems model of CC
Convex optimization primer
Reverse engr: equilibrium properties
Forward engr: FAST TCP

## Slide 101: Duality model of TCP/AQM
TCP/AQM
Equilibrium (x*,p*) primal-dual optimal:
  F determines utility function U
  G guarantees complementary slackness
  p* are Lagrange multipliers
Uniqueness of equilibrium
x* is unique when U is strictly concave
p* is unique when R has full row rank
Kelly, Maloo, Tan 1998
Low, Lapsley 1999

## Slide 102: Duality model of TCP/AQM
TCP/AQM
Equilibrium (x*,p*) primal-dual optimal:
  F determines utility function U
  G guarantees complementary slackness
  p* are Lagrange multipliers
Kelly, Maloo, Tan 1998
Low, Lapsley 1999
The underlying convex program also
leads to simple dynamic behavior

## Slide 103: Duality model of TCP/AQM
Equilibrium (x*,p*) primal-dual optimal:
Mo & Walrand 2000:
a = 1 : Vegas, FAST, STCP
a = 1.2: HSTCP
a = 2 : Reno
a = : XCP (single link only)
Low 2003

## Slide 104: Duality model of TCP/AQM
Equilibrium (x*,p*) primal-dual optimal:
Mo & Walrand 2000:
Low 2003
a = 0: maximum throughput
a = 1: proportional fairness
a = 2: min delay fairness
a = : maxmin fairness

## Slide 105: Some implications
Equilibrium
  Always exists, unique if R is full rank
  Bandwidth allocation independent of AQM or arrival
  Can predict macroscopic behavior of large scale networks
Counter-intuitive throughput behavior
  Fair allocation is not always inefficient
  Increasing link capacities do not always raise aggregate throughput
  [Tang, Wang, Low, ToN 2006]
Forward engineering: FAST TCP
  Design, analysis, experiments
[Wei, Jin, Low, Hegde, ToN 2006]

## Slide 106: Equilibrium throughput
a = 1.225 (Reno), 0.120 (HSTCP)
Reno penalizes long flows
Reno’s square-root-p throughput formula
Vegas, FAST: equilibrium cond = Little’s Law

## Slide 107: Vegas/FAST: effect of RTT error
Persistent congestion can arise due to
  Error in propagation delay estimation
Consequences
  Excessive backlog
  Unfairness to older sources
Theorem
A relative error of es in propagation delay estimation distorts the utility function to

## Slide 108: Evalidation
Single link, capacity = 6 pkt/ms, as = 2 pkts/ms, ds = 10 ms
With finite buffer: Vegas reverts to Reno
Without estimation error
With estimation error

## Slide 109: Validation
Source rates (pkts/ms)
# src1 src2 src3 src4 src5
5.98 (6)
2.05 (2) 3.92 (4)
0.96 (0.94) 1.46 (1.49) 3.54 (3.57)
0.51 (0.50) 0.72 (0.73) 1.34 (1.35) 3.38 (3.39)
0.29 (0.29) 0.40 (0.40) 0.68 (0.67) 1.30 (1.30) 3.28 (3.34)
# queue (pkts) baseRTT (ms)
19.8 (20) 10.18 (10.18)
59.0 (60) 13.36 (13.51)
127.3 (127) 20.17 (20.28)
237.5 (238) 31.50 (31.50)
416.3 (416) 49.86 (49.80)

## Slide 110: Mathematical models
Why mathematical models?
Dynamical systems model of CC
Convex optimization primer
Reverse engr: equilibrium properties
Forward engr: FAST TCP

## Slide 111: Reno design
ACK: W  W + 1/W
Loss: W  W – 0.5W
Packet level
Reno TCP
Flow level
  Equilibrium
  Dynamics
pkts
(Mathis formula 1996)

## Slide 112: Reno design
Packet level
  Designed and implemented first
Flow level
  Understood afterwards
Flow level dynamics determines
  Equilibrium: performance, fairness
  Stability
Design flow level equilibrium & stability
Implement flow level goals at packet level

## Slide 113: Forward engineering
Decide congestion measure
  Loss, delay, both
Design flow level equilibrium properties
  Throughput, loss, delay, fairness
Analyze stability and other dynamic properties
  Control theory, simulate, improve model/algorithm
Iterate 1 – 3 until satisfactory
Simulate, prototype, experiment
  Compare with theoretical predictions
  Improve model, algorithm, code
Iterate 1 – 5 until satisfactory

## Slide 114: Forward engineering
Tight integration of theory, design, experiment
Performance analysis done at design time
  Not after
Theory does not replace intuitions and heuristics
  Refines, validates/invalidates them
Theory provides structure and clarity
  Guides design
  Suggests ideas and experiments
  Explores boundaries that are hard to expt

## Slide 115: Packet level description
ACK: W  W + 1/W
Loss: W  W – 0.5W
Reno
AIMD(1, 0.5)
ACK: W  W + a(w)/W
Loss: W  W – b(w)W
HSTCP
AIMD(a(w), b(w))
ACK: W  W + 0.01
Loss: W  W – 0.125W
STCP
MIMD(a, b)
FAST

## Slide 116: Flow level: Reno, HSTCP, STCP, FAST
Different gain k and utility Ui
  They determine equilibrium and stability
Different congestion measure qi
  Loss probability (Reno, HSTCP, STCP)
  Queueing delay (Vegas, FAST)
Common flow level dynamics!
window
adjustment
control
gain
flow level
goal
=

## Slide 117: Flow level: Reno, HSTCP, STCP, FAST
Common flow level dynamics!
window
adjustment
control
gain
flow level
goal
=
Small adjustment when close, large far away
  Need to estimate how far current state is wrt target
  Scalable
Reno, Vegas: window adjustment independent of qi
  Depends only on current window
  Difficult to scale

## Slide 118: rsrg
SISL
NetLab
prof steven low
2001
2000
Lee Center
2002
2003
2004
2005
2006
FAST TCP theory
IPAM Wkp
SC02 Demo
2007
WAN-in-Lab Testbed
Caltech FAST Project
control & optimization of networks
theory
experiment
deployment
testbed
Collaborators: Doyle (Caltech), Newman (Caltech), Paganini (Uruguay), Tang (Cornell), Andrew (Swinburne), Chiang (Princeton); CACR, CERN, Internet2, SLAC, Fermi Lab, StarLight, Cisco
Internet: largest distributed nonlinear feedback control system
theory
Reverse engineering: TCP is real-time distributed algorithm over Internet to maximize utility
Forward engineering: Invention of FastTCP based on control theory & convex optimization
deployment
FAST is commercialized by FastSoft; it accelerates world’s 2nd largest CDN and Fortune 100 companies
FastTCP
TCP
Internet
FAST in a box
with FAST
without FAST
experiment
Internet2 LSR
SuperComputing BC
SC 2004
Scientists have used FastTCP to break world records on data transfer between 2002 – 2006
Lee Center
testbed
WAN-in-Lab : one-of-a-kind wind- tunnel in academic networking, with 2,400km of fiber, optical switches, routers, servers, accelerators
eq 1
eq 2
eq 3

## Slide 119: Some benefits
Transparent interaction among components
  TCP, AQM
  Clear understanding of structural properties
Understanding effect of parameters
  Change protocol parameters, topology, routing, link capacity, set of flows
  Re-solve NUM
  Systematic way to tune parameters

## Slide 120: Extreme resilience to loss
SF  New York
June 3, 2007
Heavy packet loss in Sprint network:
FAST TCP increased throughput by 120x !
Without FAST
throughput: 1Mbps
With FAST
throughput: 120Mbps

## Slide 121: 10G appliance customer data
Average download speed 8/24 – 30, 2009, CDN customer (10G appliance)
FAST vs TCP stacks in BSD, Windows, Linux

## Slide 122: Summary: math models
Integration of theory, design, experiment can be very powerful
  Each needs the other
  Combination much more than sum
Theory-guided design approach
  Tremendous progress in the last decade; not as impossible as most feared
  Very difficult; but worth the effort
  Most critical: mindset
How to push theory-guided design approach further ?
Notes: After FR/FR, when CA is entered, cwnd is half of the window when lost was detected.
So the effect of lost is halving the window.
[Source: RFC 2581, Fall & Floyd, “Simulation based Comparison of Tahoe, Reno, and SACK TCP”]

## Slide 123: Agenda
9:00 Congestion control protocols
10:00 break
10:15 Mathematical models
11:15 break
11:30 Advanced topics
12:30 lunch

## Slide 124: Advanced Topics

## Slide 125: Advanced topics
Heterogeneous protocols
Layering as optimization decomposition

## Slide 126: The world is heterogeneous…
Linux 2.6.13 allows users to choose congestion control algorithms
Many protocol proposals
  Loss-based: Reno and a large number of variants
  Delay-based: CARD (1989), DUAL (1992), Vegas (1995), FAST (2004), …
  ECN: RED (1993), REM (2001), PI (2002), AVQ (2003), …
  Explicit feedback: MaxNet (2002), XCP (2002), RCP (2005), …

## Slide 127: Some implications
 | homogeneous | heterogeneous
equilibrium | unique | ?
bandwidth allocation on AQM | independent | ?
bandwidth allocation on arrival | independent | ?

## Slide 128: Throughputs depend on AQM
FAST and Reno share a single bottleneck router
NS2 simulation
Router: DropTail with variable buffer size
With 10% heavy-tailed noise traffic
FAST throughput
buffer size = 80 pkts
buffer size = 400 pkts

## Slide 129: Multiple equilibria: throughput depends on arrival
 | eq 1 | eq 2
Path 1 | 52M | 13M
path 2 | 61M | 13M
path 3 | 27M | 93M
eq 1
eq 2
Tang, Wang, Hegde, Low, Telecom Systems, 2005
Dummynet experiment

## Slide 130: Multiple equilibria: throughput depends on arrival
 | eq 1 | eq 2
Path 1 | 52M | 13M
path 2 | 61M | 13M
path 3 | 27M | 93M
Tang, Wang, Hegde, Low, Telecom Systems, 2005
eq 1
eq 2
eq 3 (unstable)
Dummynet experiment

## Slide 131
Duality model:
Why can’t use Fi’s of FAST and Reno in duality model?
delay for FAST
loss for Reno
They use different prices!

## Slide 132
Duality model:
Why can’t use Fi’s of FAST and Reno in duality model?
They use different prices!

## Slide 133: Homogeneous protocol
F1
FN
G1
GL
R
RT
TCP
Network
AQM
x
y
q
p
same price
for all sources

## Slide 134: Heterogeneous protocol
F1
FN
G1
GL
R
RT
TCP
Network
AQM
x
y
q
p
heterogeneous
prices for
type j sources

## Slide 135: Heterogeneous protocols
Equilibrium: p that satisfies
Duality model no longer applies !
pl can no longer serve as Lagrange multiplier

## Slide 136: Heterogeneous protocols
Equilibrium: p that satisfies
Need to re-examine all issues
Equilibrium: exists? unique? efficient? fair?
Dynamics: stable? limit cycle? chaotic?
Practical networks: typical behavior? design guidelines?

## Slide 137: Notation
Simpler notation: p is equilibrium if
on bottleneck links
Jacobian:
Linearized dual algorithm:
Tang, Wang, L., Chiang, ToN, 2007
Tang, Wei, L., Chiang, ToN, 2010

## Slide 138: Existence
Theorem
Equilibrium p exists, despite lack of underlying utility maximization
Generally non-unique
  There are networks with unique bottleneck set but infinitely many equilibria
  There are networks with multiple bottleneck set each with a unique (but distinct) equilibrium

## Slide 139: Regular networks
Definition
A regular network is a tuple (R, c, m, U) for
which all equilibria p are locally unique, i.e.,
Theorem
Almost all networks are regular
A regular network has finitely many and odd number of equilibria (e.g. 1)

## Slide 140: Global uniqueness
Implication
a network of RED routers with slope inversely proportional to link capacity almost always has globally unique equilibrium
Theorem
If price heterogeneity is small, then equilibrium is globally unique

## Slide 141: Local stability
Theorem
If price heterogeneity is small, then the unique equilibrium p is locally stable
If all equilibria p are locally stable, then it is globally unique
Linearized dual algorithm:
Equilibrium p is locally stable if

## Slide 142: Summary
 | homogeneous | heterogeneous
equilibrium | unique | non-unique
bandwidth allocation on AQM | independent | dependent
bandwidth allocation on arrival | independent | dependent
Interesting characterizations of equilibrium …
But not much understanding on dynamics

## Slide 143: Efficiency
Result
Every equilibrium p* is Pareto efficient
Proof:
Every equilibrium p* yields a (unique) rate x(p*) that solves

## Slide 144: Efficiency
Result
Every equilibrium p* is Pareto efficient
Measure of optimality
Achieved:

## Slide 145: Efficiency
Result
Every equilibrium p* is Pareto efficient
Loss of optimality:
Measure of optimality
Achieved:

## Slide 146: Efficiency
Result
Every equilibrium p* is Pareto efficient
Loss of optimality:
e.g. A network of RED routers with default parameters suffers no loss of optimality

## Slide 147: Intra-protocol fairness
Result
Fairness among flows within each type is unaffected, i.e., still determined by their utility functions and Kelly’s problem with reduced link capacities
Proof idea:
Each equilibrium p chooses a partition of link capacities among types, cj:= cj(p)
Rates xj(p) then solve

## Slide 148: Inter-protocol fairness
Theorem
Any fairness is achievable with a linear scaling of utility functions

## Slide 149: Inter-protocol fairness
Theorem
Any fairness is achievable with a linear scaling of utility functions
i.e. given any x in X, there exists m s.t. an equilibrium p has x(p) = x

## Slide 150: Slow timescale control
Slow timescale scaling of utility function
scaling of end--to-end price
slow timescale update of scaling factor

## Slide 151: ns2 simulation: buffer=80pks
FAST throughput
without slow timescale control
with slow timescale control

## Slide 152: ns2 simulation: buffer=400pks
FAST throughput
without slow timescale control
with slow timescale control

## Slide 153: Advanced topics
Heterogeneous protocols
Layering as optimization decomposition

## Slide 154: The Internet hourglass
IP
Web
Search
Mail
News
Video
Audio
Friends
Applications
TCP
Ethernet
802.11
Satellite
Optical
3G/4G
Bluetooth
ATM
Link technologies

## Slide 155: But what is architecture
“Architecture involves or facilitates
  System-level function (beyond components)
  Organization and structure
  Protocols and modules
  Risk mitigation, performance, evolution
but is more than the sum of these”
“… the architecture of a system defines how the system is broken into parts and how those parts interact.”
-- John Doyle, Caltech
-- Clark, Sollins, Wroclawski, …, MIT

## Slide 156: But what is architecture
“Things that persist over time”
“Things that are common across networks”
“Forms that enable functions”
“Frozen but evolves”
“It is intrinsic but artificial”
Key features (John Doyle, Caltech)
Layering as optimization decomposition
Constraints that deconstrain
Robust yet fragile

## Slide 157: Layering as opt decomposition
Each layer designed separately and evolves asynchronously
Each layer optimizes certain objectives
application
transport
network
link
physical
Minimize response time (web layout)…
Maximize utility (TCP/AQM)
Minimize path costs (IP)
Reliability, channel access, …
Minimize SIR, max capacities, …
Notes: Network adopts a layered architecture. As a result, protocol stack for network has five layers: application, transport, network, link and physical layers. Each layer is designed separately and usually abstracted as an optimization problem. For example, TCP can be seen as a distributed algorithm to solve utility maximization problem, intradomain routing is to solve minimum cost problem. The main reason to choose a layered structure is to manage the design complexity. This has been justified by the success of communication network.

## Slide 158: Layering as opt decomposition
application
transport
network
link
physical
Application: utility
IP: routing
Link: scheduling
Phy: power
Each layer is abstracted as an optimization problem
Operation of a layer is a distributed solution
Results of one problem (layer) are parameters of others
Operate at different timescales

## Slide 159: Layering as opt decomposition
Each layer is abstracted as an optimization problem
Operation of a layer is a distributed solution
Results of one problem (layer) are parameters of others
Operate at different timescales
application
transport
network
link
physical
1) Understand each layer in isolation, assuming
other layers are designed nearly optimally
2) Understand interactions across layers
3) Incorporate additional layers
4) Ultimate goal: entire protocol stack as
solving one giant optimization problem, where
individual layers are solving parts of it

## Slide 160: Layering as opt decomposition
Network generalized NUM
Layers subproblems
Layering decomposition methods
Interface functions of primal or dual vars
application
transport
network
link
physical
1) Understand each layer in isolation, assuming
other layers are designed nearly optimally
2) Understand interactions across layers
3) Incorporate additional layers
4) Ultimate goal: entire protocol stack as
solving one giant optimization problem, where
individual layers are solving parts of it

## Slide 161: Examples
application
transport
network
link
physical
Optimal web layer: Zhu, Yu, Doyle ’01
HTTP/TCP: Chang, Liu ’04
TCP: Kelly, Maulloo, Tan ’98, ……
TCP/IP: Wang et al ’05, ……
TCP/power control: Xiao et al ’01,
Chiang ’04, ……
TCP/MAC: Chen et al ’05, ……
Rate control/routing/scheduling: Eryilmax et al ’05, Lin et al ’05, Neely, et al ’05, Stolyar ’05, Chen, et al ’05
detailed survey in Proc. of IEEE, 2006

## Slide 162: Example: dual decomposition
Design via dual decomposition
  Congestion control, routing, scheduling/MAC
  As distributed gradient algorithm to jointly solve NUM
Provides
  basic structure of key algorithms
  framework to aid protocol design
Ref:
Cross-layer design in multihop wireless networks Lijun Chen, Steven H. Low and John C. Doyle. Computer Networks Journal, Special Issue on Wireless for the Future Internet, 2010

## Slide 163: Wireless mesh network
s
i
d
j

## Slide 164: Wireless mesh network
Underlying optimization problem:
Utility to flows (s,d)
Cost of using links (i,j)
Local flow constraint
Schedulability constraint

## Slide 165: Dual decomposition
congestion control
routing
scheduling
transmission rate
xid
output queue d*
to service
utility function Uid
local congestion price
pid
neighbor congestion prices
pjd, lijd
links (i,j) to
transmit
conflict graph
link weights wij
price = queueing delay

## Slide 166: Algorithm architecture
other
nodes
conflict
graph
utility
weights
Application
Congestion Control
Routing
Scheduling/MAC
Topology Control
Mobility Management
Estimation
d*
Security Mgt
En/Dequeue
Xmit/Rcv
Radio Mgt
Physical Xmission
queue
length
local price