## Slide 1: CS 179: GPU Computing
Lecture 2: more basics
Notes: Resume – remarks:
Welcome back
Storytelling/motivational purposes
Introducing

## Slide 2: Recap
Can use GPU to solve highly parallelizable problems
Straightforward extension to C++
  Separate CUDA code into .cu and .cuh files and compile with nvcc to create object files (.o files)
Looked at the a[] + b[] -> c[] example

## Slide 3: Recap
If you forgot everything, just make sure you understand that CUDA is simply an extension of other bits of code you write!!!!
  Evident in .cu/.cuh vs .cpp/.hpp distinction
  .cu/.cuh is compiled by nvcc to produce a .o file
  .cpp/.hpp is compiled by g++ and the .o file from the CUDA code is simply linked in using a "#include xxx.cuh" call
    No different from how you link in .o files from normal C++ code

## Slide 4
.cu/.cuh vs .cpp/.hpp

## Slide 5
.cu/.cuh vs .cpp/.hpp

## Slide 6
.cu/.cuh vs .cpp/.hpp

## Slide 7
.cu/.cuh vs .cpp/.hpp

## Slide 8: Thread Organization
We will now look at how threads are organized and used in GPUs
  Keywords you MUST know to code in CUDA:
    Thread
    Block
    Grid
  Keywords you MUST know to code WELL in CUDA:
    (Streaming) Multiprocessor
    Warp
    Warp Divergence

## Slide 9: Inside a GPU
The black Xs are just crossing out things you don’t have to think about just yet. You'll learn about them later

## Slide 10: Inside a GPU
Think of Device Memory (we will also refer to it as Global Memory) as a RAM for your GPU
  Faster than getting memory from the actual RAM but still can be faster
  Will come back to this in future lectures
GPUs have many Streaming Multiprocessors (SMs)
  Each SM has multiple processors but only one instruction unit
  Groups of processors must run the exact same set of instructions at any given time with in a single SM

## Slide 11: Inside a GPU
When a kernel (the thing you define in .cu files) is called, the task is divided up into threads
  Each thread handles a small portion of the given task
The threads are divided into a Grid of Blocks
  Both Grids and Blocks are 3 dimensional
  e.g.
  dim3 dimBlock(8, 8, 8);
  dim3 dimGrid(100, 100, 1);
  Kernel<<<dimGrid, dimBlock>>>(…);
  However, we'll often only work with 1 dimensional grids and blocks
  e.g. Kernel<<<block_count, block_size>>>(…);

## Slide 12: Inside a GPU
Maximum number of threads per block count is usually 512 or 1024 depending on the machine
Maximum number of blocks per grid is usually 65535
  If you go over either of these numbers your GPU will just give up or output garbage data
  Much of GPU programming is dealing with this kind of hardware limitations! Get used to it
  This limitation also means that your Kernel must compensate for the fact that you may not have enough threads to individually allocate to your data points
    Will show how to do this later (this lecture)

## Slide 13: Inside a GPU
Each block is assigned to an SM
Inside the SM, the block is divided into Warps of threads
  Warps consist of 32 threads
  All 32 threads MUST run the exact same set of instructions at the same time
    Due to the fact that there is only one instruction unit
  Warps are run concurrently in an SM
  If your Kernel tries to have threads do different things in a single warp (using if statements for example), the two tasks will be run sequentially
    Called Warp Divergence (NOT GOOD)

## Slide 14: Inside a GPU (fun hardware info)
In Fermi Architecture (i.e. GPUs with Compute Capability 2.x), each SM has 32 cores
  e.g. GTX 400, 500 series
  32 cores is not what makes each warp have 32 threads. Previous architecture also had 32 threads per warp but had less than 32 cores per SM
Halo.cms.caltech.edu has 3 GTX 570s
  This course will cover CC 2.x

## Slide 15: Streaming Multiprocessor

## Slide 16
A[] + B[] -> C[] (again)

## Slide 17
A[] + B[] -> C[] (again)

## Slide 18
A[] + B[] -> C[] (again)

## Slide 19: Questions so far?

## Slide 20
Stuff that will be useful later

## Slide 21
Stuff that will be useful later

## Slide 22
Stuff that will be useful later

## Slide 23: Next Time...
Global Memory access is not that fast
  Tends to be the bottleneck in many GPU programs
  Especially true if done stupidly
    We'll look at what "stupidly" means
Optimize memory access by utilizing hardware specific memory access patterns
Optimize memory access by utilizing different caches that come with the GPU