## Slide 1: CS 179: GPU Computing
Lecture 4: GPU Memory Systems

## Slide 2: Last time
Each block is assigned to and executed on a single streaming multiprocessor (SM).
Threads execute in groups of 32 called warps.
  Threads in a single warp can only run 1 set of instructions at once
  Can cause divergence if threads are told to perform different tasks

## Slide 3: NVIDIA Architecture Names
Architecture Family Names
  Tesla (2006) -> Fermi (2010) -> Kepler (2012) -> Maxwell (2014) -> …
  Engineering Names: GT218 -> GF110 -> GK104 -> GM206 -> ...
Each new Architecture comes with new capabilities
  Compute Capability (CC) tells you the set of capabilities included
  1.x -> 2.x -> 3.x -> 4.x -> …
For more detail: https://developer.nvidia.com/cuda-gpus

## Slide 4
Nvidia GeForce GTX 780
Notes: Everything we’ve been talking about is the GPU core. These are made by Nvidia and are the “interesting” part of the GPU.
The global memory is not part of the GPU core, and is in this case manufactured by Samsung. Its RAM similar to what is already in your computer.
Note that not being located on the same silicon generally hurts performance. This is true for accessing global memory from the GPU, and is also (very) true for moving data to GPU over PCI-E.
Light travels about 1 foot each ns (in vacuum).

## Slide 5
GK110

## Slide 6
GK110

## Slide 7: Latency & Throughput
Latency is the delay caused by the physical speed of the hardware
CPU = low latency, low throughput
  CPU clock = 3 GHz (3 clocks/ns)
  CPU main memory latency: ~100+ ns
  CPU arithmetic instruction latency: ~1+ ns
GPU = high latency, high throughput
  GPU clock = 1 GHz (1 clock/ns)
  GPU main memory latency: ~300+ ns
  GPU arithmetic instruction latency: ~10+ ns
Above numbers were for Kepler GPUs (e.g. GTX 700 series)
For Fermi, latencies tend to be double that of Kepler GPUs

## Slide 8: Compute & IO Throughput
GeForce GTX Titan Black (GK110 based)
Compute throughput | 5 TFLOPS (single precision)
Global memory bandwidth | 336 GB/s (84 Gfloat/s)
GPU is very IO limited! IO is very often the throughput bottleneck, so its important to be smart about IO.
If you want to get beyond ~900 GFLOPS, need to do multiple FLOPs per shared memory load.
Notes: Due to design of GPU, IO and compute happen at the same time. IO is generally the bottleneck.
Based on these numbers, will GPUs perform better on algorithms will high computational density or low computational density?
This is why bank conflicts matter.
80% utilization on GPU is great. We’re up to around 93% utilization for single threaded CPU matrix multiplication (probably the most tuned optimized code).

## Slide 9: Cache
A cache is a chunk of memory that sits in between a larger pool of memory and the processor
  Often times implemented at hardware level
  Has much faster access speed than the larger pool of memory
When memory is requested, extra memory near the requested memory is read into a cache
  Amount read is cache and memory pool specific
    Regions of memory that will always be cached together are called cache lines
  This makes future accesses likely to be found in the cache
    Such accesses are called cache hits and allow much faster access
    If an access is not found in the cache, it's called a cache miss (and there is obviously no performance gain)

## Slide 10: GPU Memory Breakdown
Registers
Local memory
Global memory
Shared memory
L1/L2 cache
Constant memory
Texture memory
Read-only cache (CC 3.5)
Notes: Give brief explanation of each type of memory.
I’ll go over the most important types of memory first.

## Slide 11: Part 1
Registers
Local memory
Global memory
Shared memory
Notes: Give brief explanation of each type of memory.
I’ll go over the most important types of memory first.

## Slide 12
Memory Scope
Notes: When talking about different memory types, we need to talk about both the scope as well as the hardware implementation.
The scope is simply who can access the memory and what is the lifetime of the memory.
Notably, the hardware implementation can limit the scope (as is the case for local memory), but the scope is often limited beyond what the hardware does.

## Slide 13: Global Memory
Global memory is separate hardware from the GPU core (containing SM’s, caches, etc).
  The vast majority of memory on a GPU is global memory
  If data doesn’t fit into global memory, you are going to have process it in chunks that do fit in global memory.
  GPUs have .5 - 24GB of global memory, with most now having ~2GB.
Global memory latency is ~300ns on Kepler and ~600ns on Fermi

## Slide 14
Nvidia GeForce GTX 780
Green box is GK110, red lines are global memory
Notes: Everything we’ve been talking about is the GPU core. These are made by Nvidia and are the “interesting” part of the GPU.
The global memory is not part of the GPU core, and is in this case manufactured by Samsung. Its RAM similar to what is already in your computer.
Note that not being located on the same silicon generally hurts performance. This is true for accessing global memory from the GPU, and is also (very) true for moving data to GPU over PCI-E.
Light travels about 1 foot each ns (in vacuum).

## Slide 15: Accessing global memory efficiently
Global memory IO is the slowest form of IO on GPU
  except for accessing host memory (duh...)
Because of this, we want to access global memory as little as possible
Access patterns that play nicely with GPU hardware are called coalesced memory accesses.

## Slide 16: Memory Coalescing
Memory accesses are done in large groups setup as Memory Transactions
  Done per warp
  Fully utilizes the way IO is setup at the hardware level
Coalesced memory accesses minimize the number of cache lines read in through these memory transactions
  GPU cache lines are 128 bytes and are aligned
Memory coalescing is much more complicated in reality
  See Ch 5.2 of CUDA Handbook for more detail if you're interested but it's not required
Notes: Explain what a cache line is from perspective of CPU.
On CPU, 1 load only touches 1 cache line. On GPU, not the case.
Follow with several slides of pictures.

## Slide 17
Misalignment can cause non-coalesced access
Notes: The cross lines don’t matter, but the misalignment causes 2 loads to be done (because first loaded address is 130 rather than 120)

## Slide 18
A coalesced access!
Notes: The cross lines don’t matter, just the total number of cache lines touched.

## Slide 19: Shared Memory
Very fast memory located in the SM
Same hardware as L1 cache (will discuss later)
  ~5ns of latency
Maximum size of 48KB, but user configurable
Scope of shared memory is the block
Remember
SM = streaming multiprocessor
SM ≠ shared memory
Notes: Nvidia says shared memory latency is “roughly 100x lower”, so probably closer to 3ns, but 5ns is closer enough and easier to think about.
Why is scope of shared memory not global?

## Slide 20: Shared memory syntax
Can allocate shared memory statically (size known at compile time) or dynamically (size not known until runtime)
Static allocation syntax:
  __shared__ float data[1024];
  Declared in the kernel, nothing in host code
Dynamic allocation syntax
  Host:
    kernel<<<grid_dim, block_dim, numBytesShMem>>>(args);
  Device (in kernel):
    extern __shared__ float s[];
  For multiple dynamically sized variables, see this blog post
    Little bit more complicated and there are easy alternatives

## Slide 21: A shared memory application
Task: Compute byte frequency counts
Input: array of bytes of length n
Output: 256 element array of integers containing number of
occurrences of each byte
Naive: build output in global memory, n global stores
Smart: build output in shared memory, copy to global memory at end, 256 global stores
Notes: You could declare byte frequency counts as a “stack” variable (local) and hope L1 cache does a good job.
For algorithms where you iteratively build output, you often want to do this in shared memory.

## Slide 22: Computational Intensity
Computational intensity is a representation of how many operations must be done on a single data point (FLOPs / IO)
  Vaguely similar to the big O notation in concept and usage
  e.g)
    Matrix multiplication: n3 / n2 = n
    n-body simulation: n2 / n = n
If computational intensity is > 1, then same data used in more than 1 computation
  Do as few global loads and as many shared loads as possible
Notes: FLOP = floating point operations
IO = IO operations
blocking algorithms for matrix multiplication

## Slide 23: A common pattern in kernels
copy from global memory to shared memory
__syncthreads()
perform computation, incrementally storing output in shared memory, __syncthreads() as necessary
copy output from shared memory to output array in global memory
Notes: syncthreads works at block scope, synchronizes all warps in the block.
question: is __syncthreads needed to synchronize within a warp?
answer: not always, called warp synchronous coding. more about synchronization on friday

## Slide 24: Bank Conflicts
Shared memory is setup as 32 banks
  If you divide the shared memory into 4 byte-long elements, element i lies in bank i % 32.
A bank conflict occurs when 2 threads in a warp access different elements in the same bank.
  Bank conflicts cause serial memory accesses rather than parallel
    Serial anything in GPU programming = bad for performance

## Slide 25
Bank conflict examples
Notes: Center example would take roughly twice as long.
Bank conflicts might not seem like a huge deal (because access with 2-way bank conflict is same latency as arithmetic instruction) but can have significant effect on already partially tuned programs.

## Slide 26: Bank conflicts and strides
Stride 1 ⇒ 32 x 1-way “bank conflicts” (so conflict-free)
Stride 2 ⇒ 16 x 2-way bank conflicts
Stride 3 ⇒ 32 x 1-way “bank conflicts” (so conflict-free)
Stride 4 ⇒ 8 x 4-way bank conflicts
…
Stride 32 ⇒ 1 x 32-way bank conflict :(
Notes: Stride is distance from thread i access to thread i+1 access.
How many unique banks are accessed, and how many threads are accessing that bank

## Slide 27: Padding to avoid bank conflicts
To fix the stride 32 case, we’ll waste a byte on padding and make the stride 33 :)
Don’t store any data in slots 32, 65, 98, ....
Now we have
thread 0 ⇒ index 0 (bank 0)
thread 1 ⇒ index 33 (bank 1)
thread i ⇒ index 33 * i (bank i)
Notes: Note padding is wasting some very precious hardware, and also makes code uglier.

## Slide 28: Registers
A Register is a piece of memory used directly by the processor
  Fastest “memory” possible, about 10x faster than shared memory
  There are tens of thousands of registers in each SM
    Generally works out to a maximum of 32 or 64 32-bit registers per thread
Most stack variables declared in kernels are stored in registers
  example: float x; (duh...)
Statically indexed arrays stored on the stack are sometimes put in registers
Notes: Need to check assembly to see what is in registers.
Arrays must be statically indexed because instructions hard code register number.

## Slide 29: Local Memory
Local memory is everything on the stack that can’t fit in registers
The scope of local memory is just the thread.
Local memory is stored in global memory
  much slower than registers
Notes: What’s the downside of storing local memory in global memory?
So how can we avoid storing anything in local memory?
Answer: use less local variables than registers
yes, but we’ve seen that using more local variables can help performance (assuming the local variables in registers)
sounds like we want to have as many variables that we can put in registers and no more!
If we have more local variables then registers, then some local variables will be spilled to local/global memory. This is called register spilling and kills performance.

## Slide 30: Register spilling example
When we have enough registers, this code does 4 loads from local memory and 0 stores.
Now assume we only have 3 free registers before any of this code is executed (but don’t worry about z0 and z1)
x0 = x[0];
y0 = y[0];
x1 = x[1];
y1 = y[1];
z0 = x0 + y0;
z1 = x1 + y1;

## Slide 31: Register spilling example
x0 = x[0];
y0 = y[0];
x1 = x[1];
y1 = y[1];
z0 = x0 + y0;
z1 = x1 + y1;
starting with only 3 free registers...
cannot load y[1] until we free a register. store x1 to make space.
Now we need to load x1 again.
Register spilling cost:
1 extra load
1 extra store
2 extra pairs of consecutive
dependent instructions
Notes: Stores also have instruction dependencies (cannot use a register until the store from it is done).
The pairs of dependent instructions are the store x1, load y[1] (because we’re loading y1 into the same register that we’re storing from) and load x1, z1 = x1 + y1
There are worse spilling scenarios (what if x0 was stored?) and also better (just don’t load y1 until after computing z0), but its difficult for compiler to find optimal instruction ordering wrt spilling and dependencies.
A form of register allocation problem can be reduced to k-coloring a graph, which is NP-complete.
So, is register spilling (and any use of local memory) truly so bad for performance? Thankfully not (in small doses), due to the L1 cache.

## Slide 32: Questions?
Global memory
Local memory
Shared memory
Registers
Notes: Give brief explanation of each type of memory.
I’ll go over the most important types of memory first.

## Slide 33: Part 2
L1/L2 cache
Constant memory
Texture memory
read-only cache (CC 3.5)
Notes: Give brief explanation of each type of memory.
I’ll go over the most important types of memory first.

## Slide 34: L1 Cache
Fermi - caches local & global memory
Kepler, Maxwell - only caches local memory
same hardware as shared memory
configurable size (16, 32, 48KB)
each SM has its own L1 cache
Notes: There are PTX instructions to load global memory to indicate whether you want to put it in L1 cache.
Recommendation: Use shared memory for whatever you can think of using it for, then make the rest of the space L1.
Makes local memory much cheaper (as register spills now go into L1 which is about as fast as shared).
so a little register spilling can be OK sometimes
L1 actually merged with texture cache in Maxwell.

## Slide 35: L2 cache
caches all global & local memory accesses
~1MB in size
shared by all SM’s
Notes: can look at L1/L2 hit/miss rates in profiler to see if local memory use is problematic

## Slide 36: Constant Memory
Constant memory is global memory with a special cache
  Used for constants that cannot be compiled into program
  Constants must be set from host before running kernel.
64KB for user, 64KB for compiler
  kernel arguments are passed through constant memory

## Slide 37: Constant Cache
8KB cache on each SM specially designed to broadcast a single memory address to all threads in a warp (called static indexing)
  Can also load any statically indexed data through constant cache using “load uniform” (LDU) instruction
  Go to http://www.nvidia.com/object/sc10_cuda_tutorial.html for more details
Notes: in this contxt, static does not mean known at compile time, it mans all threads accessing the same same address.
Memory address cannot depend on threadId.
Cache is small/cheap because no writeback mechanism required.
Compiler uses LDU sometimes (const + pointer aliasing concerns)

## Slide 38: Constant memory syntax
In global scope (outside of kernel, at top level of program):
__constant__ int foo[1024];
In host code:
cudaMemcpyToSymbol(foo, h_src, sizeof(int) * 1024);

## Slide 39: Texture Memory
Complicated and only marginally useful for general purpose computation
Useful characteristics:
2D or 3D data locality for caching purposes through “CUDA arrays”. Goes into special texture cache.
fast interpolation on 1D, 2D, or 3D array
converting integers to “unitized” floating point numbers
Use cases:
Read input data through texture cache and CUDA array to take advantage of spatial caching. This is the most common use case.
Take advantage of numerical texture capabilities.
Interaction with OpenGL and general computer graphics
Notes: for general purpose computing “texture support could not have been justified if the hardware hadn’t already been there” - cuda handbook
I’ve never used textures personally, and they are the most foreign part of CUDA to me.
CUDA arrays use trick like a space filling curve

## Slide 40: Texture Memory
And that’s all we’re going to say on texture memory for now, more on future set!
It’s a complex topic, you can learn everything you want to know about it from CUDA Handbook Ch 10
Notes: complex and not super useful in my opinion

## Slide 41: Read-Only Cache (CC 3.5+)
Many CUDA programs don’t use textures, but we should take advantage of the texture cache hardware.
CC ≥ 3.5 makes it much easier to use texture cache.
  Many const restrict variables will automatically load through texture cache (also called read-only cache).
  Can also force loading through cache with __ldg intrinsic function
Differs from constant memory because doesn’t require static indexing

## Slide 42: Questions?
Registers
Global memory
Local memory
Shared memory
L1/L2 cache
Constant memory
Texture memory
Read-only cache (CC 3.5)
Notes: Give brief explanation of each type of memory.
I’ll go over the most important types of memory first.

## Slide 43: Next time....
Next lecture will be the last lecture focused on basic GPU knowledge
Few more optimization techniques
Synchronization
Will discuss GPU specific algorithms starting next week